## Slide 1
When does an optimized field become a reactor design?
Lecture 4: profiles, Pareto decisions, and the repo lab
A design becomes credible when the workflow is validated
Docs: https://sos2026-rjorge-stellarator-optimization.readthedocs.io/
CEA-IRFM / Renaissance Fusion School on Stellarators
Aix-en-Provence, 2026
Rogerio Jorge, University of Wisconsin-Madison
Repo: github.com/rogeriojorge/sos2026-rjorge-stellarator-optimization
Docs: sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 01

## Slide 2
The full loop has memory
Equilibrium
>
Boozer spectrum
>
Neoclassical
>
Coils
>
Turbulence
>
Profiles
>
Pareto
Geometry changes transport
Transport changes profiles
Profiles change objectives
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 02

## Slide 3
What is profile closure?
Profile closure
Solving whether sources, sinks, transport coefficients, and radial gradients produce consistent temperature and density profiles.
source - div(Q_neo + Q_turb) = 0
Physical meaning
The same magnetic geometry can look different once profiles and heating are allowed to respond.
What the optimizer sees
Use profile closure near the end of the loop to test the design scenario, not only the vacuum field.
Failure mode
A geometry-only winner can lose when profile stiffness or power balance is included.
A reactor design is a field plus a self-consistent plasma scenario.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 03
Refs: nonlinear turbulence optimization and integrated transport validation workflows.

## Slide 4
Modern workflows are multi-fidelity by design
Design question
Optimization interpretation
SIMSOPT
objective terms, geometry objects, and coils live in one optimization framework
JAX transport tools
differentiable metrics are useful only inside a documented claim scope
Profile closure
sources and turbulence can reverse a geometry-only ranking
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 04
Refs: Landreman et al., JOSS 6, 3525 (2021); sfincs-jax and SPECTRAX-GK public docs; Kim et al., JPP 90, 905900203 (2024).

## Slide 5
Lecture 4
PART 1. Close the loop with profiles
Field optimization changes transport
Transport changes pressure and current
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 05

## Slide 6
How to read it
Temperature and density gradients drive transport
A good field metric can underperform after closure
Read how profile feedback changes the temperature response.
Profiles turn a field optimum into a scenario
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 06
Ref: transport/profile closure logic in nonlinear turbulence optimization and T3D validation literature.

## Slide 7
How to read it
Sources, fluxes, and residuals must match
A post-hoc residual is weak evidence
A design claim needs a solved balance, not only a field metric.
Power balance is a credibility check
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 07

## Slide 8
Integrated objectives should be staged
Design question
Optimization interpretation
Early
cheap geometry and Boozer screens
Middle
coils and neoclassical metrics
Late
turbulence, particles, profiles, engineering
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 08

## Slide 9
Demo break: profile closure
Notebook break
Notebook: Neopax Profile Closure
Plot temperature response
Inspect power balance
State which quantities are screened and which are validated
Notebook path: notebooks/10_neopax_profile_closure.ipynb
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 09

## Slide 10
Lecture 4
PART 2. Pareto decisions
Many designs can be defensible
The decision weights must be explicit
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 10

## Slide 11
Reactor constraints enter as gates
Design question
Optimization interpretation
Alpha heating and losses
reactor-relevant loss gate
Wall loads and blankets
engineering and material constraint
Maintenance and access
device availability constraint
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 11

## Slide 12
What is a Pareto front?
Pareto front
The set of designs where improving one objective requires worsening at least one other objective.
no design improves all objectives at once
Physical meaning
It separates physics tradeoffs from preference choices.
What the optimizer sees
Use it to decide which weights and hard gates are steering the final selection.
Failure mode
A point on the front can still fail a validation gate that was not included in the objective.
Pareto analysis makes the design decision explicit.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 12
Ref: multiobjective SIMSOPT and single-stage stellarator optimization workflows.

## Slide 13
How to read it
Nondominated points still require priorities
Final choice needs context and validation
A Pareto front is an argument surface, not an automatic answer.
Pareto fronts need interpretation
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 13
Ref: SIMSOPT objective composition and multiobjective stellarator optimization workflows.

## Slide 14
How to read it
Changing weights changes the winner
Record weights beside every selected design
A weighted score is a value judgment with units and provenance.
Weights expose the design decision
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 14

## Slide 15
Demo break: Pareto dashboard
Notebook break
Notebook: Pareto Design Dashboard
Change one metric weight
Regenerate the chart
Defend the selected design
Notebook path: notebooks/11_pareto_design_dashboard.ipynb
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 15

## Slide 16
Validation check
Equilibrium, Boozer, neoclassical, turbulence, particles, profiles, coils, engineering
A design can pass one gate and fail the next
Validation rule: state the assumption, identify the metric, and explain what would change your mind.
Validation gates prevent metric gaming
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 16

## Slide 17
Lecture 4
PART 3. The GitHub repo is the lab manual
Slides explain concepts
Notebooks execute projects
Scripts regenerate figures, movies, and status
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 17

## Slide 18
A design is a validated workflow
The repo is the audit trail
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 18

## Slide 19
Repo lab flow
command surface
$ python scripts/run_smoke_tests.py
$ python scripts/execute_all_notebooks.py
$ python scripts/build_powerpoint_decks.mjs
$ python scripts/check_release_ready.py
python scripts/check_release_ready.py
python scripts/make_lecture_bundle.py
python scripts/audit_notebook_outputs.py
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 19

## Slide 20
Live demos and research runs have different roles
Design question
Optimization interpretation
reference examples
student reliability
short live run
instructor timing
research run
documented solver output after timing
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 20

## Slide 21
ReadTheDocs is the canonical guide
Design question
Optimization interpretation
Docs
https://sos2026-rjorge-stellarator-optimization.readthedocs.io/
Repo
github.com/rogeriojorge/sos2026-rjorge-stellarator-optimization
Use the live demo matrix during class
Use it as a metric, constraint, or validation gate.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 21

## Slide 22
Repo lab: full reference run
Notebook break
scripts/check_release_ready.py
Run acceptance checks
Review STATUS.md
Open rendered docs
Start with the reference run. Repo: https://github.com/rogeriojorge/sos2026-rjorge-stellarator-optimization | Docs: https://sos2026-rjorge-stellarator-optimization.readthedocs.io/
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 22

## Slide 23
Coil robustness returns in the final workflow
Design question
Optimization interpretation
Manufacturing tolerance
can the design survive perturbations?
Current errors
can operations maintain the target field?
Thermal and mechanical deformation
does the coil story remain true?
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 23

## Slide 24
There is no single best stellarator
There are only defensible choices with stated priorities
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 24

## Slide 25
Exercise: change the weights and defend a design
Notebook break
Notebook: Pareto Design Dashboard
Move one weight
Identify the new winner
Say which validation gate you now trust less
Notebook path: notebooks/11_pareto_design_dashboard.ipynb
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 25

## Slide 26
Documentation is part of reproducibility
Design question
Optimization interpretation
README
how a student starts
ReadTheDocs
the rendered guide during class
STATUS.md
data provenance and claim scope
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 26

## Slide 27
Lecture 4
APPENDIX. Lecture 4 checks and replacements
Use this section before distributing the school bundle
Keep claim scope visible
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 27

## Slide 28
What belongs in git
Design question
Optimization interpretation
Small inputs
versioned and documented
Small inputs
versioned and documented
Large outputs
regenerated by scripts and ignored
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 28

## Slide 29
Validation check
Original package PDFs and PPTX files
Private screenshots and huge generated media
Local environments and secrets
Validation rule: state the assumption, identify the metric, and explain what would change your mind.
What stays out of git
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 29

## Slide 30
STATUS.md anatomy
Design question
Optimization interpretation
Package status
what imported and what was skipped
Data status
source, hash, and provenance
Notebook status
what ran and saved outputs
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 30

## Slide 31
Validation check
A package starts compiling during class
A notebook loses its reference data path
A result is numerical but the validation path is missing
Validation rule: state the assumption, identify the metric, and explain what would change your mind.
Live-demo abort criteria
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 31

## Slide 32
Animation storyboard: optimization history
Read the sequence as objective residual decreasing
Discuss when a live animation adds value
Static storyboard for reliable projection; the movie file remains in the repo.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 32

## Slide 33
Manual steps before the school
Design question
Optimization interpretation
Choose the lecture machine and environment
Use it as a metric, constraint, or validation gate.
Pre-fetch equilibria and verify notebooks render
Use it as a metric, constraint, or validation gate.
Freeze the branch or tag used for the school
Use it as a metric, constraint, or validation gate.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 33

## Slide 34
How students should use the repo after school
Design question
Optimization interpretation
Start with reference results
reproduce every figure
Change one notebook at a time
Use it as a metric, constraint, or validation gate.
Keep generated outputs small and documented
Use it as a metric, constraint, or validation gate.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 34

## Slide 35
How to read it
Use to discuss profile-closure behavior
Keep the limitation explicit
Reference plot for profile closure discussion.
Reference figure: profile closure
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 35

## Slide 36
How to read it
Use to discuss the final design choice
Ask which design the room would defend
Reference plot for design-decision discussion.
Reference figure: Pareto front
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 36

## Slide 37
Final design commandments
Show every boundary with its coil story
State the validation domain for every metric
Pair each proxy with its failure mode
Show the weights behind each Pareto choice
A good optimization result is a design argument that survives new metrics.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 37

## Slide 38
Coupled, differentiable, reproducible stellarator design
Field, coils, transport, profiles, and decisions in one auditable loop
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
optimization workflow
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 38

## Slide 39
Lecture 4
What to remember
Keep the scientific object and the computed artifact together
Rerun, perturb, compare, and explain before trusting the optimum
Docs: https://sos2026-rjorge-stellarator-optimization.readthedocs.io/
Repo lab handoff: rerun, perturb, compare, explain.
github.com/rogeriojorge/sos2026-rjorge-stellarator-optimization
sos2026-rjorge-stellarator-optimization.readthedocs.io
Slide 39