## Slide 1
Transport physics becomes optimization metrics
Lecture 3: neoclassical, turbulence, fast-particle metrics
Neoclassical, turbulence, and fast particles enter as screens and validation gates
The goal is to use the physics responsibly inside a design loop
CEA-IRFM / Renaissance Fusion School on Stellarators
Aix-en-Provence, 2026
Rogerio Jorge, University of Wisconsin-Madison
Slide 01

## Slide 2
Lecture 3
PART 1. A hierarchy of transport calculations
Cheap screens remove poor designs early
Expensive calculations validate finalists
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 02

## Slide 3
Cost hierarchy for transport metrics
Geometry metrics are fast
Boozer and effective-ripple metrics screen designs
DKE, gyrokinetics, particles, and profiles validate finalists
Cost hierarchy
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 03

## Slide 4
Neoclassical recap for optimizers
01
Symmetry breaking produces trapped-particle radial drifts
02
Effective ripple compresses one transport risk
03
Ambipolar electric fields and bootstrap current matter
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 04

## Slide 5
How to read it
Useful: fast, profile-like, interpretable
Limit: still followed by transport matrices or experiments
Use the figure to identify the design choice and the diagnostic that changes.
Example: effective ripple comparison
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 05

## Slide 6
NEO-JAX and SFINCS-JAX have different roles
Design question
Optimization interpretation
NEO_JAX
compact effective-ripple diagnostics
SFINCS_JAX
richer drift-kinetic validation
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 06

## Slide 7
Notebook project: SFINCS-JAX cached validation
Computational project
notebooks/07_sfincs_jax_neoclassical_cached.ipynb
Read a collisionality scan
Inspect Er roots
Plot a bootstrap-current proxy
1
Open
2
Run cached
3
Change one knob
4
Explain the plot
Deliverable: one figure and one defensible sentence.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 07

## Slide 8
How to read it
Transport coefficients change across regimes
Suppression mechanisms are profile and field dependent
Use the figure to identify the design choice and the diagnostic that changes.
Example: cached neoclassical scan
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 08

## Slide 9
How to read it
Multiple roots can imply different impurity and turbulence behavior
Optimization records the root choice
Use the figure to identify the design choice and the diagnostic that changes.
Example: ambipolar Er roots
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 09

## Slide 10
How to read it
Bootstrap current can change equilibrium and island risk
It depends on profiles and collisionality
Use the figure to identify the design choice and the diagnostic that changes.
Example: bootstrap-current constraint
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 10

## Slide 11
W7-X motivates neoclassical optimization
01
Reduced neoclassical losses are a stellarator-design success
02
The next bottleneck can still be turbulence
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 11

## Slide 12
Lecture 3
PART 2. Turbulence metrics
Use linear calculations as early screens
Compare with nonlinear validation when rankings matter
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 12

## Slide 13
The turbulence question is a fidelity ladder
Linear growth: fast screen
Quasilinear weights: ranking hypothesis
Nonlinear heat flux: expensive validation
Profiles: performance closure
Cost hierarchy
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 13

## Slide 14
Notebook project: SPECTRAX-GK linear metric
Computational project
notebooks/08_spectrax_gk_linear_metric.ipynb
Plot growth rate versus ky rho_i
Plot mode frequency
State the range of validity of the proxy
1
Open
2
Run cached
3
Change one knob
4
Explain the plot
Deliverable: one figure and one defensible sentence.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 14

## Slide 15
How to read it
Growth-rate peaks indicate instability drive
They are followed by nonlinear heat-flux checks
Use the figure to identify the design choice and the diagnostic that changes.
Example: linear growth-rate spectrum
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 15

## Slide 16
How to read it
Growth and frequency together are more informative than growth alone
The sign and trend help identify mode families
Use the figure to identify the design choice and the diagnostic that changes.
Example: linear mode frequency
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 16

## Slide 17
Notebook project: proxy versus validation
Computational project
notebooks/09_turbulence_metric_surrogate.ipynb
Choose the best design by each metric
Compare the rankings
Discuss why rankings differ
1
Open
2
Run cached
3
Change one knob
4
Explain the plot
Deliverable: one figure and one defensible sentence.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 17

## Slide 18
How to read it
A proxy may rank designs differently from nonlinear validation
The optimizer receives whatever metric you give it
Use the figure to identify the design choice and the diagnostic that changes.
Example: proxy versus nonlinear validation
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 18

## Slide 19
How to read it
Neoclassical success can leave turbulent limits
Profile response can saturate performance
Use the figure to identify the design choice and the diagnostic that changes.
Example: W7-X ion-temperature-gradient clamping
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 19

## Slide 20
Lecture 3
PART 3. Fast particles and validation gates
Reactors require alpha-particle confinement
Particle metrics must be rerun after coil design changes
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 20

## Slide 21
Fast particles are reactor gates
01
Present experiments may tolerate losses that reactors cannot
02
Alpha confinement, wall loads, and orbit classes enter late-stage validation
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 21

## Slide 22
Particle metrics connect back to coils
01
Coil errors can alter field topology
02
Fast-particle diagnostics should be rerun after coil design changes
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 22

## Slide 23
Metric trust ladder
screen
ranking hypothesis
validation calculation
experiment or integrated scenario
Cost hierarchy
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 23

## Slide 24
Validation check
Does the metric fail on a known bad design?
Does it rank a known good design correctly?
Does it change smoothly under small perturbations?
Classroom rule: label approximations, keep cached mode ready, and write down what was actually computed.
Validation compares failure modes
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 24

## Slide 25
Computational checkpoint for lecture 3
Computational project
scripts/execute_all_notebooks.py
Run notebooks 07, 08, 09
Record which curves are cached
Replace one cached column only if a real run is timed
1
Open
2
Run cached
3
Change one knob
4
Explain the plot
Deliverable: one figure and one defensible sentence.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 25

## Slide 26
Exercise: choose early and late metrics
Try this
5-10 minute classroom exercise
Which metric screens 1000 designs?
Which metric validates five finalists?
What is the failure mode of each?
Expected answer is qualitative: identify the tradeoff, not a magic optimum.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 26

## Slide 27
Exercise: proxy versus nonlinear ranking
Try this
5-10 minute classroom exercise
Select the proxy optimum
Select the validation optimum
Explain why the optimizer might prefer the wrong one
Expected answer is qualitative: identify the tradeoff, not a magic optimum.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 27

## Slide 28
Lecture 3 notebook map
Design question
Optimization interpretation
03 effective ripple
Use it as a metric, constraint, or validation gate.
07 neoclassical validation
Use it as a metric, constraint, or validation gate.
08 linear GK metric
Use it as a metric, constraint, or validation gate.
09 turbulence surrogate
Use it as a metric, constraint, or validation gate.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 28

## Slide 29
Five rules from lecture 3
Use cheap screens early
Validate with richer physics late
Plot profiles and regimes
Never hide proxy failure
Record the trust ladder
A good optimization result is a design argument that survives new metrics.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 29

## Slide 30
Neoclassical outputs to track
Design question
Optimization interpretation
Effective ripple
low-collisionality transport screen
Ambipolar roots
radial electric-field validation
Bootstrap current
profile-dependent equilibrium feedback
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 30

## Slide 31
Turbulence outputs to track
Design question
Optimization interpretation
Linear growth rate
fast instability screen
Quasilinear weight
ranking hypothesis
Nonlinear heat flux
validation for finalists
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 31

## Slide 32
Fast-particle outputs to track
Design question
Optimization interpretation
Alpha confinement
reactor-relevant loss gate
Wall loads
engineering and material constraint
Orbit classes
topology-sensitive diagnostic
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 32

## Slide 33
Validation check
Use them to compare trends and failure modes
Use real code for numerical thresholds
Document which physics was omitted
Classroom rule: label approximations, keep cached mode ready, and write down what was actually computed.
Cached transport metrics teach the hierarchy
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 33

## Slide 34
Discussion: what can reverse the ranking?
01
A neoclassical winner can lose on turbulence
02
A turbulence winner can fail alpha confinement
03
A profile change can move both metrics together
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 34

## Slide 35
Research path: NEO_JAX and SFINCS_JAX
Choose the same equilibrium and flux surface
Scan collisionality and radial electric field
Compare compact metrics before detailed validation
Record roots, bootstrap current, and sensitivity
Cost hierarchy
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 35

## Slide 36
Research path: SPECTRAX-GK
Start with a tiny linear calculation
Plot growth rate and frequency versus ky
Compare proxy rankings with nonlinear expectations
Keep the nonlinear validation gate explicit
Cost hierarchy
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 36

## Slide 37
Example - W7-X as a validation reminder
01
Neoclassical optimization is necessary
02
Ion-temperature clamping motivates turbulence checks
03
Profiles decide whether the metric matters experimentally
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 37

## Slide 38
Metric trust ladder
Design question
Optimization interpretation
Screen
cached or reduced model trend
Ranking hypothesis
tiny or quasilinear run
Validation
expensive run or experimental comparison
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 38

## Slide 39
Validation check
Growth rate screens instability before heat-flux validation
A scalar ripple value should point back to where losses occur
A profile proxy should lead to a solved discharge model
Classroom rule: label approximations, keep cached mode ready, and write down what was actually computed.
How to read a fast metric
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 39

## Slide 40
Example - profile dependence enters early
01
Collisionality depends on density and temperature
02
Bootstrap current changes equilibrium assumptions
03
Turbulent heat flux changes the temperature profile
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 40

## Slide 41
Before showing a transport number
Design question
Optimization interpretation
Equilibrium
which surface and which profiles?
Kinetics
which species and collisionality?
Validation
which expensive calculation confirms it?
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 41

## Slide 42
Exercise extension - choose two gates
01
Pick an early screen that runs in class
02
Pick a validation gate for finalists
03
Explain which design could fail each gate
Class use
Connect the concept to one objective, one plot, and one exercise.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 42

## Slide 43
Transport metrics are gates, not decorations
Use cheap metrics to steer the search
Use expensive metrics to challenge finalists
Always record the physics omitted by the shortcut
A good optimization result is a design argument that survives new metrics.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 43

## Slide 44
Lecture 3 take-home messages
Neoclassical, turbulence, and particles enter at different costs
A design ranking is only as strong as its validation ladder
Profile assumptions should be visible on every transport claim
A good optimization result is a design argument that survives new metrics.
SOS 2026 Stellarator Optimization, Rogerio Jorge, UW-Madison
cached / tiny / research
Slide 44

## Slide 45
Lecture 3
Take-home message
Keep the scientific object and the computed artifact together
Rerun, perturb, compare, and explain before trusting the optimum
Repo lab handoff: rerun, perturb, compare, explain.
Slide 45